## Slide 1
Reporter：Nie Yongxin , She Xiaoliang , Chang Yi
The characteristics of MOSFET BSC520N15NS3

## Slide 2
The division of labour
Nie Yongxin: make the ppt & collect the data
Chang Yi: make the ppt & collect the data
She Xiaoliang: make the ppt & collect the data

## Slide 3
Simulation Model
Parameter Setup
Simulation Results
Analysis of the Results
01.
02.
03.
04.
Catalog

## Slide 4
01
Simulation Model

## Slide 5
Simulation model 1
01
This model is established to find out the Output characteristics, Drain-source on resistance, Transfer characteristics and Switching waveform of MOSFET BSC520N15NS3 device. It includes a resistor, two voltage sources, a MOSFET BSC520N15NS3. The connection is shown on the ppt.

## Slide 6
01
When VGS and VDS get a series of different values, we can get a bunch of curves of ID, which is the Output characteristics.
When VGS gets a series of different values, VDS is fixed and we simulate at different temperatures, we can get a bunch of curves of ID , which is Transfer characteristics.
When we simulate Time-domain simulation, VGS being pulsating signal, we can get switching waveform correspondingly .
When VGS and VDS get a series of different values, we can get a bunch of curves of ID,and then divide VDS by ID to get RDS(on) , which is Drain-source on resistance.

## Slide 7
01
Simulation model 2
This model is established to find out the forward characteristics of reverse diode of MOSFET BSC520N15NS3 device.
It includes a resistor, one voltage source, a MOSFET BSC520N15NS3.

## Slide 8
When VDS gets a series of different values at different temperatures, we can get different curves of IF.

## Slide 9
02
Parameter Setup

## Slide 10
02
Parameter Setup
2 Drain-source on resistance
1
VDS start value: 0 stop value: 3 increment: 0.1
VGS start value: 4 stop value: 10 increment: 0.5
R = 1
1 Output characteristics
2
VDS start value: 0 stop value: 20 increment: 0.1
VGS start value: 5 stop value: 10 increment: 1
R = 1

## Slide 11
3
4
3 Transfer characteristics
VGS start value: 0 stop value: 8 increment: 0.8
Tj start value: 25 stop value: 150 increment: 125
VDS = 150
R = 1
4 Forward characteristics
of reverse diode
VSD start value: 0 stop value: 2 increment: 0.1
Tj start value: 25 stop value: 150 increment: 125
R = 1

## Slide 12
5
5 Switching waveform
VDC = 10
R = 1
VGS

## Slide 13
Simulation Results
03

## Slide 14
1
Output characteristics

## Slide 15
2
Drain-source on resistance

## Slide 16
3
Transfer characteristics

## Slide 17
4
Forward characteristics of reverse diode

## Slide 18
5
Switching waveform

## Slide 19
04
Analysis of the Results

## Slide 20
1
Output characteristics
Compared with the output characteristics given by datasheet, the images are approximately identical.
When the VGS is bigger than 4.5V, the larger the VGS, the larger the ID, and tend to saturation with the increase of VDS.

## Slide 21
2
Drain-source on resistance
Compared with drain-source on resistance given by datasheet, the images are approximately identical.
RDS(on) decreases with the increase of VGS, and increases with the increase of ID.

## Slide 22
3
Transfer characteristics
Compared with transfer characteristics given by datasheet, the images are approximately identical.
The higher the temperature is, the smaller the voltage required for MOSFET conduction.

## Slide 23
4
Forward characteristics of reverse diode
Compared with transfer characteristics given by datasheet, the images are approximately identical.
The IF of reverse diode increases with temperature and tends to saturation with the increase of VSD.

## Slide 24
5
Switching waveform
The transmission delay of MOSFET BSC520N15NS3 is nanosecond. Since the period of VGS is also nanosecond, the waveform will show the charging and discharging process of interelectrode capacitance, so the waveform is not regular square wave.

## Slide 25
Thank you